A. If removing Plenum chamber plus cylinder head (if only detaching Plenum Chamber start at B)

Remove the bonnet (not necessary if only removing Plenum Chamber – not sure if needed if removing head)

Depressurise the fuel system by disconnecting the fuel pump fuse (A1 15amp) and the black/white wire from both distributors. Crank the engine for approximately 15 seconds.  Turn off the battery master switch.

B. Detaching Plenum Chamber  to replace vacuum pipes

Turn off the battery master switch.

Position a container under the cylinder block drains then remove the coolant filler cap, open both cylinder block drain taps and drain the engine cooling system.

Remove the four dome-headed bolts securing the fuel rail cover. On early cars retrieve and retain the four spacers fitted between the cover and plenum top.

Disconnect the by-pass hoses from the air intake manifold to the idle air valves.

Remove the large bore trunking from the air intake manifold to the throttle bodies.

Disconnect the electrical connections to the following;

Injectors (8)

Throttle potentiometer

Idle air valves

Air temperature sensors

Cam sensors (both distributors)

RPM sensor ‘B’ bank distributor.

Remove the eight injector retaining clips.

Disconnect the fuel rail fuel inlet and return lines.

Remove the six M6 setscrews, spring washers and plain washers securing the fuel rail to the six pillars and lift off the fuel rail. Remove the pillars.

Remove the eight injectors.

Remove the two M6 bolts and setscrews, spring and plain washers securing each throttle body to the plenum chamber, disconnect the throttle bodies from the throttle linkage and remove the throttle bodies.

Remove the four M8 socket headed cap screws and the ten dome-headed bolts from the plenum chamber top.

Locate the cover splitter in the plenum throttle body aperture then gently tighten the cover adjuster bolt until the plenum chamber top comes free. Lift off the plenum chamber top.

Remove the front and rear locating dowels.

Remove the eight 1/4in socket headed cap screws securing each inlet manifold assembly and remove the manifolds.

Lift and ease the plenum base forward to allow access to the vacuum pipes connected to the underside of the base.

C. Continue if removing the entire cylinder head

Disconnect the fuel regulator and absolute pressure vacuum pipes from the base.

Disconnect the brake vacuum hose at the non-return valve.

Disconnect the water hoses to the rear of the cylinder heads.